## Slide 1: Overview of differences and gaps of Lawful Interception between legacy telecommunication and multimedia call scenarios
S3LI01-112

## Slide 2: Identifiers
Identifiers used to select a target to be intercepted
PSTN: Directory Number
2G Networks (CS and PS): MSISDN, IMSI, IMEI
3G CS and PS domain: MSISDN, IMSI, IMEI
3G IMS domain: SIP URL

## Slide 3: Intercepting network elements
2G Networks, 3G CS and PS domain
  MSC (MSC Server)
  GSN
3G IMS domain
  P-CSCF
  S-CSCF

## Slide 4: Result of Interception
  PSTN, 2G networks and 3G CS/3G PS domain:
    Intercept related information (IRI) describing the event and the parties involved is delivered on interface port X0_2.
    Content of communication (CC) is delivered on interface port X0_3.
  3G IMS domain:
    Only intercept related information describing the event and the parties involved can be delivered on interface port X0_2, content of communication is not available at CSCF.

## Slide 5: Correlation issues
A subscriber can (and should) be intercepted in both domains: PS and IMS domain.
A correlation between interception results from PS domain with results from IMS domain is only possible with the "lawful interception identifier" which may be unique for a subscriber, but not for a call. As no interception specific signaling is available, no exchange of interception data between intercepting nodes is possible.

## Slide 6: Location Dependent Interception
Location Dependent Interception (LDI) is a feature for serving nodes like VMSC, VMSC-Server and SGSN to intercept a subscriber only in a given area the Law Enforcement Agency is authorized for.
In P-CSCF and S-CSCF the location of the subscriber is not known. This means that a subscriber always will be intercepted, independent of his location, as long as an interception task is entered in the CSCF.

## Slide 7: Interception and Call Forwarding
Scenario: Not intercepted subscriber A calls intercepted subscriber B which has call forwarding conditional (e.g. busy) to not intercepted subscriber C.
In case of CS the visited MSC (Server) of intercepted subscriber B will intercept the call.
In case of multimedia call in IMS domain the node (S-CSCF) responsible for intercepted subscriber B will return the new directory number for not intercepted subscriber C to not intercepted subscriber A. Not intercepted subscriber A will establish a new call to not intercepted subscriber C. This call will not be intercepted as node for intercepted subscriber B is not involved any longer and no interception specific signaling between the nodes is available.